## Slide 1: Digital Signals

## Slide 2: Digital Signals
Use binary (0s and 1s) to encode information
sequence of voltage pulses (DC levels) – each pulse represents a signal element
binary data are transmitted using only 2 types of signal elements
( 1 = positive voltage, 0 = negative voltage )
Usually aperiodic; period and frequency are not appropriate
Less affected by interference (noise); fewer errors

## Slide 3: Digital signal

## Slide 4
Information in a digital signal can be represented in the form of voltage levels.
A Signal can have more than two levels
if a signal has L levels then, each level need Log2L bits

## Slide 5: A digital signal with four levels

## Slide 6: Bit Interval and Bit Rate
Digital signals are described by
Bit interval or Bit length– time required to send one single bit
    Bit Length = propagation speed * bit duration
Bit rate – number of bit intervals per second, usually expressed as bits per second (bps)
Bit rate = 1 / Bit interval

## Slide 7
Baud Rate
It is the rate of Signal Speed, i.e. the rate at which the signal changes.
A digital signal with two levels ‘0‘ & ‘1‘ will have the same baud rate and bit rate

## Slide 8: Three signals with different bit rates and baud rates
a)Signal with a bit rate of 8 bits/ sec and baud rate of 8 baud/sec
b) Signal with a bit rate of 16 bits/ sec and baud rate of 8 baud/sec
c) Signal with a bit rate of 16 bits/ sec and baud rate of 4 baud/sec

## Slide 9: Digital signal As a Composite Analog Signal
Digital signal, with all its sudden changes, is actually a composite analog signal having an infinite number of frequencies
The bandwidth of a digital signal is infinite i.e. A digital signal is a composite signal with an infinite bandwidth.

## Slide 10: Digital signal through a wide bandwidth medium
if a medium has a wide bandwidth, a digital signal can be sent through it
Some frequencies will be weakened or blocked by medium; still, enough frequencies will be passed to preserve a decent signal shape
Such as a coaxial cable to send a digital signal through a LAN

## Slide 11: Digital signal through a band-limited medium
the Internet via telephone line
The relationship between bite rate (n) and the required bandwidth (B)
Using only one harmonic
Using more harmonic

## Slide 12: Using only one harmonic (Digital versus Analog)

## Slide 13: TYPES OF CHANNELS
Each composite signal has a lowest possible(minimum) frequency and a highest possible (maximum) frequency.
From the point of view of transmission, there are two types of channels:
Low pass Channel
  This channel has the lowest frequency as ‘0‘ and highest frequency as some non-zero frequency ‘f1‘.
  This channel can pass all the frequencies in the range 0 to f1.
Band pass channel
  This channel has the lowest frequency as some non-zero frequency ‘f1‘ and highest frequency as some non-zero frequency ‘f2‘.
  This channel can pass all the frequencies in the range f1 to f2.

## Slide 14: Lowpass Channel & Bandpass Channel

## Slide 15: Transmission of Digital signal
Digital signal can be transmitted in the following two ways:
Baseband Transmission
the signal is transmitted without making any change to it
sending a digital signal over a channel without changing the digital signal to an analog signal i.e. without modulation
Requires that we have a low-pass channel, a channel with a bandwidth that starts from zero.
This is the case if we have a dedicated medium with a bandwidth constituting only one channel.
In baseband transmission, the bandwidth of the signal to be transmitted has to be less than the bandwidth of the channel.

## Slide 16
Ex. Consider a Baseband channel with lower frequency 0Hz and higher frequency 100Hz, hence its bandwidth is 100 Hz
We can easily transmit a signal with frequency below 100Hz, such a channel whose bandwidth is more than the bandwidth of the signal is called Wideband channel
Logically a signal with frequency say 120Hz will be blocked resulting in loss of information, such a channel whose bandwidth is less than the bandwidth of the signal is called Narrowband channel

## Slide 18: Low-Pass Channel with Wide Bandwidth
To preserve the exact form of a nonperiodic digital signal with vertical segments vertical and horizontal segments horizontal, we need to send the entire spectrum, the continuous range of frequencies between zero and infinity.
This is possible if we have a dedicated medium with an infinite bandwidth between the sender and receiver that preserves the exact amplitude of each component of the composite signal.
If a coaxial cable or fiber optic, with a very wide bandwidth is used, then two stations can communicate by using digital signals with very good accuracy.

## Slide 20: Low-Pass Channel with Limited Bandwidth
In a low-pass channel with limited bandwidth, we approximate the digital signal with an analog signal.
The level of approximation depends on the bandwidth available.
Rough Approximation
Assume that we have a digital signal of bit rate N.
Consider the worst case, a maximum number of changes in the digital signal.
  sequence 01010101 ... or the sequence 10101010…..
  To simulate these two cases, we need an analog signal of frequency f = N/2.

## Slide 22
The two similar cases (000 and 111) are simulated with a signal with frequency f =0 and a phase of 180° for 000 and a phase of 0° for 111.
The two worst cases (010 and 101) are simulated with an analog signal with frequency =N/2 and phases of 180° and 0°.
The other four cases can only be simulated with an analog signal with f = N/4 and phases of 180°, 270°, 90°, and 0°.
In other words, we need a channel that can handle frequencies 0, N/4, and N/2. This rough approximation is referred to as using the first harmonic (N/2) frequency.

## Slide 23
To make the shape of the analog signal look more like that of a digital signal, we need to add more harmonics of the frequencies.
i.e. to increase the bandwidth to 3N/2, 5N/2, 7N/2, and so on.

## Slide 24
Broad band Transmission
Given a bandpass channel, a digital signal cannot be transmitted directly through it
In broadband transmission we use modulation, i.e. we change the signal to analog signal before transmitting it.
Modulation allows us to use a bandpass channel-a channel with a bandwidth that does not start from zero.

## Slide 25
The digital signal is first converted to an analog signal, since we have a bandpass channel we cannot directly send this signal through the available channel.
Ex. Consider the bandpass channel with lower frequency 50Hz and higher frequency 80Hz, and the signal to be transmitted has frequency 10Hz.
To pass the analog signal through the bandpass channel, the signal is modulated using a carrier frequency. Ex. The analog signal (10Hz) is modulated by a carrier frequency of 50Hz resulting in an signal of frequency 60Hz which can pass through our bandpass channel.
The signal is demodulated and again converted into an digital signal at the other end

## Slide 26: Modulation of a digital signal

## Slide 27
A digital signal is converted to a composite analog signal with the help of carrier.
At the receiver, the received analog signal is converted to digital, and the result is a replica of what has been sent.

## Slide 28: Broadband Transmission Involving Modulation & Demodulation