## Slide 1: SDLC & HDLC

## Slide 2: Synchronous Data Link Communication (SDLC)
Synchronous Bit Oriented Protocol by IBM.
Simplex/half duplex/full duplex.
Sliding window protocol.
Language EBCDIC.
Data frame 256 characters long.
All data link control functions performed by a single control field.
Master-slave environment only.

## Slide 3
The primary station controls data exchange on the communication channel and issues command.
The secondary station receives commands and returns responses to the primary.
Three transmission states:-
  Transient state:-before and after the initial transmission and after each line turnaround.
  Idle state:- after 15 or more consecutive 1s have been received.
  Active state:- whenever either primary or secondary station is transmitting information or control signals.

## Slide 4: General frame structure:
Flag | Address | Control | Data… | FCS | Flag
8 bits | 8 bits | 8 bits | Variable multiples of 8 | 16 bits | 8 bits

## Slide 5: High-level Data Link Control HDLC
HDLC is a discipline for the management of information transfer over a data communication channel
HDLC has a basic structure that governs the function and the use of control procedures. The basic structure includes:
  The definitions of primary and secondary station responsibilities.
  The design of information grouping for control and checking.
  The design of the format for transfer of information and control data.

## Slide 6
Primary and secondary stations
A data link involves two or more participating stations. For control purposes one station on the link is designated a primary station, the others are secondary stations.
The primary station is responsible for the organisation of data flow and for the link level error recovery procedures.
A frame sent from a primary station is referred to as a command frame. A frame from a secondary to a primary is referred to as a response frame.
Normally when a command is sent, a response or a string of responses is expected in reply

## Slide 7: HDLC Station Types
Primary station
  Controls operation of link
  Issues commands (frames)
  Maintains separate logical link to each secondary station
Secondary station
  Under control of primary station
  Issues responses (frames)
Combined station
  May issue commands and responses
  Combines the features of primary and secondary stations

## Slide 8: HDLC Link Configurations
Unbalanced
  One primary and one or more secondary stations
  Supports full duplex and half duplex
Balanced
  Two combined stations
  Supports full duplex and half duplex

## Slide 9: Frame Structure
Synchronous transmission
All transmissions in frames
Single frame format for all data and control exchanges

## Slide 10: Types of frames
There are three kinds of frames:
I-frame: Information frame: This type of frame carries user’s data.
S-frame: Supervisory frame: used for error and flow control.
  This is used for supervisory control functions such as acknowledgements, requesting transmission and requesting a temporary suspension of transmission.

## Slide 11
U-frame: Unnumbered frame or Unsequenced frame:
  Unnumbered frames are used for link management. This is used to provide additional link control functions.
  Used to set up the logical link between the primary station and a secondary station
  To inform the secondary station about the mode of operation which is used.

## Slide 12: Frame Structure
01111110
01111110
Defines 3 types of frames (I,S,U frames)

## Slide 13: Flag Fields
Delimit frame at both ends
01111110
Receiver hunts for flag sequence to synchronize
Bit stuffing used to avoid confusion with data containing 01111110
  The transmitter inserts 0 bit after every sequence of five 1s with the exception of flag fields
  If receiver detects five 1s it checks next bit
    If 0, it is deleted
    If 1 and seventh bit is 0 (i.e., 10), accept as flag
    If sixth and seventh bits 1 (i.e., 11), sender is indicating abort

## Slide 14: Bit Stuffing
Example with possible errors

## Slide 15: Address Field
Identifies secondary station that sent or will receive frame
Usually 8 bits long
May be extended to multiples of 7 bits
  LSB of each octet indicates that it is the last octet (1) or not (0)
All ones (11111111) is broadcast

## Slide 16: Control Field
Different for different frame type
  I-frame (information frame)
    data to be transmitted to user (next layer up)
    Flow and error control piggybacked on information frames
  S-frame (Supervisory frame)
    Used for flow and error control
  U-frame (Unnumbered frame)
    supplementary link control
First one or two bits of control filed identify frame type

## Slide 17: Control Field Diagram

## Slide 18: Poll/Final Bit
Use depends on context
Command frame
  P bit : used for poll from primary
  1 to solicit (poll) response from peer
Response frame
  F bit : used for response from secondary
  1 indicates response to soliciting command

## Slide 19: I-frame
Contains the sequence number of transmitted frames and a piggybacked ACK
1 2 3 4 5 6 7 8
0
N(S)
P/F
N(R)
I,0,0
I,1,0
I,2,0,P

## Slide 20: S-frame
Used for flow and error control
1 2 3 4 5 6 7 8
1
S
P/F
N(R)
RR --- receive ready
RNR --- receive not ready
REJ --- reject on frame N(R)
SREJ --- selective reject on N(R)
0

## Slide 21: U-frame
Mode setting, recovery, connect/diconnect
1 2 3 4 5 6 7 8
1
M
P/F
M
1
Unnumbered function bits

## Slide 22: Unnumberred frames
Set normal response mode (SNRM)
Set asynchronous response mode (SARM)
Set asynchronous balanced mode (SABM)
Disconnect (DISC)
Unnumberred acknowledgement (UA)
Disconnect mode (DM)
Request disconnect (RD)
Unnumberred poll (UP)
Reset (RSET)
Exchange identification (XID)
Test (TEST)
Frame reject (FRMR)

## Slide 23: Information Field
Only in information and some unnumbered frames
Must contain integral number of octets
Variable length

## Slide 24: Frame Check Sequence Field
FCS
Error detection
16 bit CRC
Optional 32 bit CRC

## Slide 25: Data link channel states
Active channel state:
A channel is in an ACTIVE state when the primary or a secondary is actively transmitting a frame, a single abort sequence or interframe time fill. In this state the right to continue transmission is reserved.
Abort:
A station can abort a frame by transmitting at least seven contiguous ones. The receiving station will ignore the frame.
Interframe time fill:
In this state continuous flag bytes are sent between frames.
Idle channel state:
A channel is defined to be in an IDLE state when the transmission of 15 or more contiguous one bits is detected. In this state a primary must repoll a secondary before transmitting an I-frame to it.

## Slide 26: Modes of operation
Normal response mode
  In this mode a secondary station can transmit only in response to a command frame from the primary station.
  The response transmission may consist of one or more frames, the last of which must be explicitly indicated (using the Poll/Final bit).
  The secondary then cannot transmit again until it receives another command to do so.

## Slide 27
Asynchronous Response Mode (ARM)
  In this mode the secondary station may initiate transmission of a frame or group of frames without receiving explicit permission from the primary.
  The frames may contain data or control information.
  The secondary station is responsible for time-out and retransmission if necessary.
Asynchronous Balanced Mode (ABM)
  In this mode the stations have identical protocols. They both can initiate transmission at any time.
  They can send both commands and responses.

## Slide 28: HDLC Operation
Exchange of information, supervisory and unnumbered frames
Three phases
  Initialization
  Data transfer
  Disconnect

## Slide 29: Examples of Operation (1)

## Slide 30: Examples of Operation (2)

## Slide 31
Internet consists of individual systems that are connected to each other.
Basically, it is wide area network that is built up from point-to-point leased lines.
In these point-to-point lines, two major data link protocols are used:
Serial Line Internet Protocol (SLIP)
Point-to-Point Protocol (PPP)

## Slide 32: The Data Link Layer in the Internet
A home personal computer acting as an internet host.

## Slide 33: Serial Line Internet Protocol (SLIP)
It is a means of sending Internet Protocol datagrams over a serial link.
It can be used by two systems to communicate via a direct cable connection or modem link.
The initial purpose of this protocol was to connect Sun workstation to the Internet over a dial-up line using modem.

## Slide 34: Point-to-Point Protocol (PPP)
PPP was devised by IETF (Internet Engineering Task Force) to create a data link protocol for point-to-point lines that can solve all the problems of SLIP.
It is the most commonly used data link protocol.
It is used in dial up connection to connect the home PC to the ISP server.
Point to point, wired data link easier to manage than broadcast link: no Media Access Control
PPP is extremely simple (the simplest in the Data Link protocol family) and very streamlined

## Slide 35: Differences Between SLIP & PPP